## Slide 1: BALLARD* Closed Suction Systems Paediatrics

## Slide 2: BALLARD* Closed Suction Systems Paediatrics
Luc Van Audenhove Head of Marketing
Reworked version from Tommy Lynch
Zaventem, October 2023;

## Slide 3
The information provided in the AirLife Training Academy for the Sales and Marketing teams of AirLife and its distributors is not intended for further distribution.
The enclosed information can only be used for educational purposes for our sales teams.
This information can under no circumstances be used as advertising or for distribution to end users.
Confidential: Not for further distribution

## Slide 4: BALLARD* Closed Suction System for Pediatric & Neonate
Objectives:
Describe the special needs of neonates that are on Mechanical Ventilation.
Understand the AirLife solution for closed suction catheters for neonates.
State the features of Neonatal CSS.

## Slide 5: Neonate Population
An infant less than a month old
Special Considerations:
            Mechanical Ventilation is different
            Suctioning is markedly different
            Vital signs are much more likely to change
Notes: Neonates
Premature Infants
  Premature infants often require ballot or a support because their lungs are not fully functional and may lack surfactant, a chemical produced by the body that keeps the lungs inflated.
High Pregnancy/labor/delivery complications
  Delivery complications place a huge amount of stress on the neonate and the stress often leads to respiratory failure and the need for ventilation
Fetal stress
  Labor complications
  Delivery
Meconium aspiration
  Meconium aspiration occurs when the neonate takes a breath during the delivery process when the airway is filled with the baby’s first bowel movement. In general terms, it is aspiration of fecal material. Fecal material is caustic to the lungs and causes respiratory failure. Mechanical ventilation and suctioning will resolve this aspiration.

## Slide 6: NICU and PICU
Nursing Staff:
  One on One nursing
  Extremely protective
  Rarely float nurses
  Highly motivated and educated
  Critically evaluate new techniques and products
Notes: Same as the pervious slide in regards characteristics of the NICU & PICU environment you will need to be aware of and follow.

## Slide 7: NICU
Population - Neonatal Issues:
  Immature lungs
  Decreased or no surfactant
  Increased work of breathing
  Ventilator complications
    Barotrauma/Volutrauma
    Infection
  Low body temperature
Notes: The slide describes more information about the patient population
Neonatal Symptoms
Immature lungs
Decreased / no surfactant
  Discussed on previous slide
Increased work of breathing
  This comes from the lack of surfactant. Surfactant makes it easy to breathe and neonates without surfactant struggle to survive.
Ventilator complications
  Barotrauma / lung damage
    Discussed during adult ventilation. Barotrauma is pressured trauma from a high ventilating pressures which leads to lung damage.
  Infection
    Ventilation and intubation often lead to VAP, even in neonates
Body temperature
  Neonates have very thin skin and lose body heat quickly. They are kept warm with special lights and incubators.

## Slide 8: NICU
Premature Infants:
Under gestational age (full term is 40 weeks)
Organ Systems are not completely developed
      Lungs begin producing surfactant at 26 weeks
      Immune System develops at 32 weeks
      Lungs increase production of surfactant at 38 weeks
      GI System is still immature at 34 weeks
Immunosuppressed
Notes: This is a photograph of a neonate.
The neonate is not just a miniature adult
  It is a premature infant
  Its body organs including lungs, heart, brain, GI tract, kidneys, liver and skin are not completely developed. Clinicians are where of these development issues and care for the patient accordingly.

## Slide 9: NICU and PICU
Ventilation Strategies:
Continuous Positive Airway Pressure (CPAP) – may minimize ventilator associated lung injury.
Conventional Mechanical Ventilation – complex interrelationship among the ventilator, blood gas values, mechanical characteristics of the respiratory system and the infant’s spontaneous respiratory efforts.
Manipulating Peak Inspiratory Pressure (PIP), Positive End Expiratory Pressure (PEEP), Rate, Flow and others.
Notes: Take a brief moment and think back to the review we had on Mechanical Ventilation…remember all of the different types of ventilators and strategies associated with this patient population?

## Slide 10: NICU and PICU
Strategies to prevent lung injury:
Immature and developing lungs are particularly susceptible to acquired lung injuries
Emphasis is being placed on evidence that suggests lung injury partially depends on the particular ventilator strategies used.
  Prevent Volutrauma caused by too high volumes,
  Prevent repeated collapse (Atelectasis) and reopening of the alveoli.

## Slide 11: NICU and PICU
Alternative modes of ventilation: Technologic advances have resulted in better ventilators:
  Patient-Triggered Ventilation
  Synchronized Intermittent Mandatory Ventilation (SIMV)
  Proportional Assist Ventilation
  Volume Targeted Ventilation
  Tracheal Gas In-sufflation
  High Frequency Ventilation (HFV)
    High frequency jet ventilation (HFJV)
    High frequency flow interruption (HFFI)
    High frequency oscillatory ventilation (HFOV)
  The Modes of Ventilation for the NICU and PICU are different for that of the Adult Patient Population
Notes: The Modes of Ventilation for the NICU and PICU are different for that of the Adult Patient Population

## Slide 12: Why is suctioning necessary in this patient population?
Like the adult, the neonate is not able to spontaneously remove secretions from the airways.
Mechanical Suctioning is required to:
  Remove secretions from the (artificial) airway; including mucous plugs
  Improve gas exchange
Notes: Why is suctioning necessary and neonates?
The patient cannot spontaneously remove secretions from the airways.
Mechanical Suctioning:
Removes secretions from the (artificial) airway
Improves gas exchange
Reduces opportunity of pneumonia

## Slide 13: BALLARD* Closed Suction System Pediatric & Neonatal
Clinical Concerns:
Desaturation: - Hypoxia - Cardiac Arrythmias
Infection: - Death - Risk is higher with intubation and ventilation = VAP
Airway trauma: - Potential is increased without measured depth suctioning and excessive vacuum pressures
Psychological trauma: - Neonates stress very easily
Efficacy: - Time
Cost: - Less focus on cost in the NICU
Notes: review clinical concerns relative to the neonate:
Desaturation
  Hypoxia
  Cardiac arrhythmias
  Death
Infection
  Risk is higher with intubation and ventilation = VAP
Airway trauma
  Potential is increased without measured depth suctioning and excessive vacuum pressures
Psychological trauma
  Neonates stress very easily
Efficacy of TRACH CARE*
  Does it work
  Time
Cost
  Less focus on cost in the NICU in the past however that is changing

## Slide 14: BALLARD* Closed Suction System Pediatric & Neonatal
Suctioning Complications:
  Desaturation leading to Hypoxia:
    Cardiac Arrhythmia
    Hemodynamic change
    Neurological impairment
  Loss of lung recruitment therapy:
    Barotrauma
    Extended ventilator/ICU time
Notes: Complications of Suctioning
Desaturation > Hypoxia
  Cardiac Arrhythmia's
  Hemodynamic changes
  Neurological impairment
Loss of lung recruitment therapy
  Barotrauma
  Extended ventilator/ICU time
Infection
  Antibiotic regime
  Extended ventilator/ICU time leads to VAP
Airway Trauma
  Hemorrhage
  Pneumothorax
Psychological stress on baby
Death- rare but can happen.

## Slide 15: BALLARD* Closed Suction System for Pediatric & Neonatal
Suctioning Complications:
  Infection
    Antibiotic regime
    Extended time on ventilator/ICU time
  Airway Trauma
    Hemorrhage
    Pneumothorax
  Psychological Stress
  Death

## Slide 16: Value Propositions - Three Key Messages
2. Improve Patient Care
3. Efficient and Effective Procedure
1. Reduced Infections

## Slide 17: Value Proposition:
Reduced Infections:
Reduce opportunity for procedure related infections: VAP,
Protect care-giver from contamination,
Reduce patient to patient cross contamination,
Maintain a closed vent circuit.
Notes: Infection Control
Reduce opportunity for procedure related infections -VAP
Protect care-giver from contamination
Reduce pt-pt cross contamination
Maintain closed vent circuit
These are the same issues that we discussed for the adult TRACH CARE* market and they are the same for the neonatal market as well.

## Slide 18: Value Proposition:
Improve Patient Care: Physiologic
Maintains O2 delivery: Reduces desaturation (Hypoxemia)
Maintains PEEP (positive airway pressure): Reduces alveolar de-recruitment
Reduces cardiac arrhythmias
< O2 consumption
Intra-cranial pressures ICP
Notes: This is a list of the physiological advantages of using neonatal TRACH CARE* (cont’d).
Maintains O2 delivery
  Reduces desaturation (Hypoxemia)
Maintains PEEP (positive airway pressure)
  Reduces alveolar de-recruitment
Reduces cardiac arrhythmias
< O2 consumption
Intra-cranial pressures ICP

## Slide 19: Value Proposition:
Improve Patient Care: Psychological
Ventilator breathing maintained
Shortened procedure time
More gentle catheter insertion – less traumatic
Less stress for the patient
Notes: This is a list of the psychological advantages of using neonatal TRACH CARE*. Discuss each briefly.
Ventilator breathing maintained
Shortened procedure time
More gentle catheter insertion – less traumatic
Less stress for the patient

## Slide 20
Efficient and Effective Procedure: Time
One person suction technique
Reduces procedure time
Less stress patient
Standardization of procedure
Value Proposition:
Notes: This is a list of the time advantages of using neonatal TRACH CARE*. Discuss each briefly.
One person suction technique
Reduces procedure time.
Less stress patient
Standardization of procedure

## Slide 21
Efficient and Effective Procedure: Cost
Reduce cost of treating complications associated with ventilated high-risk babies
  Hypoxemia
  Cardiac
  Infection
Comparison costs of TRACH CARE* vs. multiple single use catheters
Reduced procedure time
Value Proposition:
Notes: This is a list of the cost advantages of using neonatal TRACH CARE*. Discuss each briefly.
Reduce cost of treating complications associated with ventilated high risk babies
  Hypoxemia
  Cardiac
  Infection
Comparison costs of TRACH CARE* vs. multiple single use catheters
Reduced procedure time

## Slide 22: Closed Suction System for Pediatric and Neonatal Products
Neonatal CSC
  Neonatal Y (195, 196, 197,198)
  Neonatal Elbow (202, 206, 207, 208)
  Neonatal Manifold (201, 200, 205)
Notes: Now let’s review neonatal TRACH CARE* products. The neonatal product line includes three major categories including neonatal Trached Care, pediatric TRACH CARE*, and MAC catheters.
Point to the photograph with a laser pointer and ask the class to identify the TRACH CARE* products.
From left to right:
Neonatal TRACH CARE* “Y” configuration
MAC Catheter
Neonatal TRACH CARE* Manifold configuration
Neonatal TRACH CARE* Elbow configuration

## Slide 23: BALLARD* Closed Suction System for Pediatric & Neonate
Tip to tale:

## Slide 24: BALLARD* Closed Suction System for Pediatric & Neonate
Features:
24-hour use.
Low dead-space adapters: Manifold & Y adapter designed with low dead space and direct the catheter down the ETT.
PEEP Seal prevents ventilator gases from entering the soft suction sleeve.
Soft tactile sleeve allows for a precise touch and feel of the suction catheter for gentle measured depth suctioning.
All BALLARD* Paediatric & Neonate CSC include numeric and color striped markings for precise measured depth suctioning.
Isolated suction valve: The thumb control well prevents secretions and bacteria from migrating back into the suction catheter and endotracheal tube.
Notes: The older Manifold had an issue with dead space that may have derailed conversions several years ago. All adapters are now designed with low dead space adapters and they direct the catheter down the ETT.
A 6 Fr CSS includes 2.5, 3.0 and 3.5 adapters.
A 3.0 ETT requires a 6Fr suction Catheter. Twice the ETT value to determine Fr. Size.
We always include the exact adapter (based on Fr. Size) and 0.5 mm below and 0.5 mm above the exact adapter.
PEEP Seal
  Same as adult TRACH CARE*. Prevents ventilator gases from entering the soft suction sleeve
Soft tactile sleeve
  Allows for a precise touch and feel of the suction catheter for gentle measured depth suctioning
Measured Suction
  All neonatal and pediatric TRACH CARE* catheters include numeric and color striped markings for precise measured depth suctioning
Isolated suction valve
  The thumb control well prevents secretions and bacteria from migrating back into the suction catheter and endotracheal tube.

## Slide 25: Directions for Use
Notes: Hands-on product demos. Make sure that the each group of two to three people have the following items:
Clear head
TRACH CARE** (DSE or T-Piece)
Saline bullets
Exam gloves

## Slide 26: Tips & Tricks

## Slide 27: BALLARD* Closed Suction System for Pediatric & Neonate
Inspect
Do not flood HME
Stop withdrawal when black mark on tip of catheter is visible in the dome.
Do not re-sterilize
Single use
Time usage
Inspect saline vial
Rx Only
Select appropriate size
Don’t block airway
Appropriate vacuum
Use appropriate suction times
Use caution in every vent mode
Tips & Tricks

## Slide 28: Tips & Tricks
Choosing the Appropriate Size Catheter:
Directions for Use (DFU):
Select the appropriate size CSC catheter. Most experts suggest that the catheter selected should occupy no more than one half of the internal diameter of the artificial airway.
Rule of thumb choosing catheter size:
    2 X ETT size mm
  Example:
    3,0 mm ETT x 2 = 6 Fr Closed Suction Catheter
Notes: Choosing the appropriate size catheter
The relationship of suction catheter (OD) to the ET tube
Rule of thumb cath size:
  2 times ET size mm, 8.0mm tube (x2) = 16F
  Choose next lowest size catheter or 14 French
14 French is the most common
Most respiratory therapists know this rule of thumb and sometimes will deviate from it. It’s their call.
This is a safety rule of thumb that prevents use of oversized suction catheters.
A suction catheter should never exceed 50% of the endotracheal tube diameter. This allows the patient to be ventilated during the suctioning procedure.

## Slide 29: Tips & Tricks
Warning:
Fully withdraw the CSC catheter before cutting endotracheal tube, otherwise, the catheter may also be cut.
Notes: Warnings
Continuous flow therapy and T-Piece.
Great care should be taken when cutting the endotracheal tube. Many hospitals trim the endotracheal tube to reduce kinking and lower the inspiratory pressures. ** they should always make certain that the TRACH CARE** catheter is fully withdrawn into the sleeve before cutting the endotracheal tube. This can be confirmed by visualization of the black stripe on the catheter within the clear suction sleeve. Noted with arrow in photograph.

## Slide 30: Tips & Tricks
E.T Tube Markings
Catheter Markings
Measured Depth Technique:
Notes: Measured Depth Suction
The reason for measured suction in neonates is to prevent inadvertent damage to the carina. The neonates carina is thin and easily punctured with a suction catheter. Measured suctioning prevents the suction catheter from being introduced to far into the trachea.
Measured depth suctioning includes aligning the numbers marked on the endotracheal tube with the numbers or colors marked on the suction catheter. This ensures that the suction catheter does not extend beyond the endotracheal tube tip. The hospital we’ll have a policy and procedure that dictates the distance the catheter can extend beyond the endotracheal tube. The common distances are 0.0, 0.5 and 1.0 cm relative to the endotracheal tube.
Point out alignment of numbers on ET tube and catheter as one method for positioning catheter tip at ET tube tip.]

## Slide 31: Tips & Tricks:
Note where tip of ET tube adapter is in relation to ET tube:
“Window”
Measured Depth Suctioning
# at adapter tip + 5 = # at window
Notes: This is a photograph of the neonatal TRACH CARE* “Y” adapter highlighting the features that allow the clinician to perform precise measured depth suctioning.
Can be used to point out how numbers align during safe suction procedure.
Measure 5mm back from the adapter tip. Practice with a CSS before going into presentation or in-service. Tell the clinicians to do the same!
Pass a catheter and adapter around for visualization by everyone.
The lavage port is directly over the PEEP Seal.

## Slide 32: Closed Suction – Measured Depth Suction – Special Ventilators – NICU
Examples are based on different sizes of ET tubes:
CMV Ventilator – Drager
  3.0 ET Tube x 2 = 6 FR Catheter
  Add on 5 for Adapter
HFO Vent – Oscillator
  3.0 ET Tube x 2 = 6 FR Catheter
  Add on 8 for Adapter
“Jet” Vent
  2.5 ET Tube x 2 = 5.0 FR Catheter
  Add on 6 for Adapter
  Most facilities will practice the numbers matching on CSC to ETTube.
Notes: Data from
Northwestern Memorial Hospital – NICU
These are very popular vents that you will often see utilized in the NICU/PICU in your facilities.
You will need to know these formulations not only while maintaining business for Pediatric TRACH CARE* but for educational in-services. It is not always just adding on 5 for the adapter, it is based on what vent they are using to determine the best measured depth suctioning.

## Slide 33: Clinical Evidence

## Slide 34: Clinical Evidence

## Slide 35: Decreasing the adverse effect (AE) of endotracheal suctioning (ES) during mechanical ventilation (MV) by changing practice
Prospective open 4-month study:
  229 consecutive pediatric ICU patients
    Alternate months format
    BALLARD* CSS versus open suction
Local Policy required 2 nurses for open suction
Data collected for:
ES event, staff, duration, saline use, HR, MP, SpO2, AEs
Conclusions:
Compared with open ES, ES by CSS caused less physiologic disturbances, similar AE frequency, and required less staff time and fewer nurses.
This evidence supported change of ICU practice to CSS as standard
Chart: 
| Staff time/day (min) | Decreased SpO2 (%) | Increased MAP (%) | Increased HR (%)
Closed | 23 | 4.8 | 3.4 | 1.6
Open | 38 | 6.3 | 9.2 | 4.6
6691 ES events
Open vs closed ES
  583 vs 441 patient-days
  6.0 vs 7.2 ES events/day (p < 0.01)
  Mean ES duration 2.6 min vs 3.2 min
  ES time/day per nurse 38 min vs 23 min (p < 0.01)
  ↓SpO2 6.3% vs 4.8% (p = 0.01)
  ↑HR 4.6% vs 1.6%, (p < 0.01)
  ↑MAP 9.2% vs 3.4% (p < 0.01)
Evans J et al. Aust Crit Care 2014;27:70–74.

## Slide 36: BALLARD* CSS Paediatric & Neonate Sales & Marketing tools

## Slide 37: BALLARD* Closed Suction System for Pediatric & Neonate
HC659-04
HC692-01

## Slide 38: Thank You