## Slide 1: Medication Delivery

## Slide 2: Agenda
Nebulizer overview
Where used
Small Volume Nebulizers
  Nebulizer Setup and Components
  Key Components and Terms
  CareFusion SVN Brands
  High Efficiency Nebulizers
  Competitive Landscape
Continuous Nebulizers

## Slide 3
Medication Nebulizer Overview

## Slide 4: What is a medication nebulizer?
A device used to administer medication in the form of an aerosol (mist) inhaled into the lungs.
Used for the treatment of asthma, COPD and other respiratory diseases
Notes: Micron = micrometer = one-millionth of a meter = one-thousandth of a millimeter (0.001 mm or 0.000039 inches)

## Slide 5: Why would somebody need medication delivered via nebulizer?

## Slide 6: How does a nebulizer work?
Uses oxygen, compressed air or ultrasonic power to break up medical solutions/suspensions into small aerosol droplets that can be inhaled directly from the device.
Particle size is important too
  Desired range is between 1 and 5 microns
Micron = micrometer
= one-millionth of a meter
= one-thousandth of a millimeter
= 0.001 mm or .000039 in
Notes: Micron = micrometer = one-millionth of a meter = one-thousandth of a millimeter (0.001 mm or 0.000039 inches)

## Slide 7: A Word on Particle Size
> 5μm impaction
Deposited into oropharynx and swallowed
1 - 5μm sedimentation
Optimal for delivery to the lower airways
<0.8 μm
Likely to be exhaled by tidal breathing
Nasal Cavity
5.8μm – 9.0μm
Pharynx
4.7μm – 5.8μm
Trachea & Primary Bronchi
4.7μm – 5.8μm
Secondary Bronchi
2.1μm – 3.3μm
Terminal Bronchi
1.1μm – 2.1μm
Alveoli
0.43μm – 0.65μm
Pharmacotherapy 2010;30(6): 562-584

## Slide 8: Commonly Used Medications
Albuterol Sulfate
  Bronchodilator – Relaxes muscles and opens breathing passages in the lungs
  Used to treat ongoing Asthma attacks
Budesonide
  Steroid - works to prevent and minimize the severity of asthma attacks
Cromolyn Sodium
  Mast Cell Stabilizer – prevents the release of histamine when patients come in contact with irritants
  Prevents asthma attacks and bronchospasms that are caused by exercise, pollutants, etc.

## Slide 9: Nebuliser – Type of Nebulizer
Small Volume Nebuliser
Uses air to pressurize the drugs in the
Medication cup into small, consistent size.
MMD – mass median density is usually
Between 1.5microns to 2.0microns
Benefits : Micron size improves the
drug delivery
Large Volume Nebulisers
Used to nebulise water into fine mist
Not used for drug delivery, but aerosolized
Water supports mild breathing distress for
Some patients.
Benefits: simple, drug free support for
non-acute conditions.
Jet Nebulisers
Acts like a piston forcing air through the
Medication cup and forcing the drugs out into
The mouthpiece like a fine mist.
Benefits : size of particles delivered.
Ultrasonic Nebulisers
Sometimes use water to conduct high Frequency vibrations into medication Cup which forces drug into a “fog”
Benefits: considered to have more
Consistent particle size….

## Slide 10: Vyaire - 3 Types of Medication Nebulizers
Small Volume Nebulizers Jet Small Volume Nebuliszer
Continuous Nebulizers

## Slide 11: Misty Finity® Continuous Nebulizer
US Annual Sales: $2.65M
Small Volume: 1-2 hours of treatment time
Medium Volume: 2-4 hours of treatment time
Large Volume: Up to 8 hours of treatment time
Medium Volume
Small Volume
Large Volume

## Slide 12: Where are Nebulisers used ?
Pre-hospital areas & Homecare
Intra-hospital areas
Ambulances / Paramedics
to support breathing & deliver aerosolized drugs
Home to treat; Chronic Asthma & Chronic pulmonary disease
Emergency
To support patient’s Respiratory distress
Stepdown units
Continue drug delivery
Maintenance of disease
ICU
Deliver Sufactant to maintain Alveola integrity
Respiratory wards
Support Cystic fibrosis
Control & stabilize asthma

## Slide 13
Medication Nebulizers Small Volume Nebulizers

## Slide 14: Small Volume Nebulizer Setup
Connect oxygen tube to the gas source and to the bottom of the SVN
Connect the top of the SVN to a T-piece
Connect the 6” flex tube to one end of the T-piece, and the mouthpiece attached to the other end
If the patient is unable to use a mouthpiece, the SVN can be attached to an aerosol mask
Notes: Hand out a MM10 to everyone an have them put it together; explain each of the components they see; sketch out how the neb works

## Slide 15: How does a nebulizer work?
Notes: Micron = micrometer = one-millionth of a meter = one-thousandth of a millimeter (0.001 mm or 0.000039 inches)

## Slide 16: Medication Nebulizer Key Terms
Mass Median Aerodynamic Diameter (MMAD) = Considered to be the average particle diameter by mass
Respirable Fraction = The fraction of the inhaled particles that penetrates into the alveolar region of the lung (1-5 microns)
Residual/Remaining Drug Volume = Medication that remains in a small volume nebulizer after the device is no longer producing mist
Treatment Time = Refers to how long it took to administer the dose of medication

## Slide 17: MMAD – Mass Median Aerodynamic Diameter
Not all averages are equal.
Mode = most frequent
Median = in the centre of the distribution
Mean = total sum / sample size
1,1,1,1,2,2,2,2,3,3,3,3,4,4,4,4,5,5,5,5,6,6,6,6,7,7,7,7,7,8,8,8,8
Mean
Sum = 151
Count = 33
151 / 33 = 4.58
Mode
Median
50% below
50% Above

## Slide 18: AirLife Medication Delivery Products
Quiz 1
What is MMAD?
Mass Median Aerodynamic Diameter
What is the desired particle size range?
1 - 5μm
What is “respirable fraction?”
inhaled particles that penetrates into the alveoli
What are the three types of medications most often used in a nebulizer (not the three generic names)
Albuterol Sulfate, Budesonide, Cromolyn Sodium

## Slide 19: Misty Max 10 Details
Launched in 2004
18 million units sold each year in US
  Largest selling small volume nebulizer in the United States
Performance Specifications
  MMAD = 1.6 µ
  % particles 1µ>5µ: 85%
  Treatment time: 8 to 10 minutes in a non-controlled clinical setting

## Slide 20: Misty Max 10 Codes
15% units
P/N | MM10 | Tee adapter | O2 tubing | Mouth piece | Flex tube | Filter | Ped Mask | Adult Mask
002430 | X |  |  |  |  |  |  | 
002431 | X | M/M |  |  |  |  |  | 
002434 | X | M/M | 7 | X |  |  |  | 
002435 | X | M/F | 7 | X | X |  |  | 
002437 | X | M/M |  | X |  |  |  | 
002438 | X | M/M | 7 | X | X |  |  | 
002439 | X | M/M | 14 | X | X |  |  | 
002442 | X | M/M |  |  |  |  |  | 
002445 | X | M/M | 7-UC | X |  |  |  | 
002446 | X | M/M | 7-UC | X | X |  |  | 
002447 | X | VLVDTEE | 7 |  |  |  |  | 
002450 | X | “Y” | 7 | X | X | X |  | 
002443 | X |  |  |  |  |  | X | 
002444 | X |  | 7 |  |  |  | X | 
002440 | X |  |  |  |  |  | Elephant | 
002455 | X |  | 7 |  |  |  | Elephant | 
002432 | X |  |  |  |  |  |  | X
002433 | X |  | 7 |  |  |  |  | X
57% units
11% units
8% units
Now with 15 languages!
Notes: Explain that anything without a tee adaptor is attaching into a mask; that one comes with a Y tee adaptor and filter to limit harmful medication from going into the ambient air, the difference in the 7 foot tubing and the you-connect-it tubing, that some come with the flex tube, and that we have two peds masks and one adult mask
BREAK after this slide

## Slide 21
Misty Fast

## Slide 22: AirLife Misty Fast Small volume nebulizer

## Slide 23: Misty Fast Details
Launched in 2013
Key Focus Product for AirLife
Performance Specifications
  MMAD = 2.4 µ
  % particles 1µ>5µ: 72%
  Treatment time: Nebulizes a standard 3ml dose in under 4 minutes

## Slide 24: What Differences & Similarities do you notice?
Air entrainment port on Misty Fast cap
Swivel mouthpiece with built-in Tee adaptor
Modified Jet Design
Flextube is the same
Reservoir holds the same volume of medication
Jet stems have different sized openings, although they may look the same
A-Nebulizer Cap, B-Jet, C-Neb bottle, D-Jet stem
MM10
Misty Fast
Notes: Pass out sample to each and have them break out into teams. Assemble them and write down every difference/similarity they see when compared to Misty Max 10

## Slide 25: Misty Fast Jet Detail
Jet has been modified for Misty Fast – improves output
Recommended 8 Lpm flow rate for optimal performance
Misty Fast jet is orange; Misty Max 10 jet is blue
MM10
Misty Fast
Notes: Have them split into teams and write down all the differences they see. This is not part of the quiz totals, but designed

## Slide 26: What the differences mean
Swivel Mouthpiece
Air Entrainment Port
Modified Jet Design
Ability to use the Misty Fast while lying in the beach chair position
Reduction in treatment time

## Slide 27: What the differences mean
Not intended for use:
In line with a circuit
Outside of the hospital
In conjunction with high flow treatment

## Slide 28: Watch the Misty Fast in Action
www.carefusion.com/mistyfast
Notes: What will the audience be able to do after this training is complete? Briefly describe each objective how the audience will benefit from this presentation.

## Slide 29: AirLife Misty Fast small volume nebulizer
M Max PN | M Fast PN | Neb | Tee adapter | O2 tubing | Mouth piece | Flex tube | Filter | Ped Mask | Adult Mask
2430 |  | X |  |  |  |  |  |  | 
2431 | FN2431 | X | M/M |  |  |  |  |  | 
2434 | FN2434 | X | M/M | 7 | X |  |  |  | 
2435 |  | X | M/F | 7 | X | X |  |  | 
2437 |  | X | M/M |  | X |  |  |  | 
2438 | FN2438 | X | M/M | 7 | X | X |  |  | 
2439 | FN2439 | X | M/M | 14 | X | X |  |  | 
2442 |  | X | M/M |  |  |  |  |  | 
2445 | FN2445 | X | M/M | 7-UC | X |  |  |  | 
2446 | FN2446 | X | M/M | 7-UC | X | X |  |  | 
2447 |  | X | VLVDTEE | 7 |  |  |  |  | 
2450 |  | X | “Y” | 7 | X | X | X |  | 
2443 |  | X |  |  |  |  |  | X | 
2444 | FN2444 | X |  | 7 |  |  |  | X | 
2440 |  | X |  |  |  |  |  | Elephant | 
2455 | FN2455 | X |  | 7 |  |  |  | Elephant | 
2432 |  | X |  |  |  |  |  |  | X
2433 | FN2433 | X |  | 7 |  |  |  |  | X
Now with 15 languages!

## Slide 30: AirLife Medication Delivery Products
Quiz 2
Name two of the physical differences between Misty Max 10 and Misty Fast
Air entrainment port, Swivel mouthpiece with built-in Tee, Modified Jet Design, Jet stems - different sized openings
How does Misty Fast work, compared to Misty Max ?
Entrainment port increases pressure & amount of drug nebulised
When can Misty Fast not be used? Name 2 scenarios
With vent circuit & at home
A customer wants to convert Misty Max cat#s 002438, 002439 and 002445 to Misty Fast. What Misty Fast codes should they order?
same with FN at start

## Slide 31: Activity hands on set up neb flow meter, saline open kits use them

## Slide 32: Why should a customer convert to Misty Fast?
Time Savings = Cost Savings
www.carefusion.com/mistyfast

## Slide 33: Misty Fast Landing Page
http://staging.interactive.columnfivemedia.com/carefusion/misty-fast/

## Slide 34: Misty Fast Sales Tools
Sales Tools Available
Brochure
Time savings calculator
Animation Video
Customer Messaging Presentation (Whitepaper executive summary)
Additional Resources
Tech bulletins
Whitepaper

## Slide 35: AirLife Medication Delivery Products
Quiz 3
What is the primary benefit of Misty Fast to a customer?
  reduced treatment time
Name at least 3 ways converting to Misty Fast has benefited customers? Don’t need specific numbers?
more time back, improved workflows, reduced AFM (cost )
What is the most important resource you can use to help with conversions?
Whitepaper?... Int = Cost calc

## Slide 36: Medication Delivery Products
AirLife filtered nebulizer system*
Only product available that has been tested with tested with the drug, Pentamidine
Pentamidine is used to treat PCP, a very serious form of pneumonia commonly found in patients with AIDS
Target Price: $5.80 / unit
P/N | Description | Packaging
124030EU | AirLife filtered nebulizer system | 20 / Case
* Formerly known as Respirgard II neb system

## Slide 37: Appendix

## Slide 38
Medication Nebulizers Small Volume Nebulizers Competitive Overview

## Slide 39: Standard SVN Competition
Intersurgical
Cirrus 2
Salter
Nebutech
Hudson
Micromist

## Slide 40: Small Volume Nebulizer - Competition
Intersurgical
Cirrus 2
  Basic SVN
  ASP: $0.74 chamber only
  ASP: $1.17 with Mask
  Strong on Contract
  Multiple kit configurations
    High-Efficiency Option (Hot top)
    ASP: $1.50
  Handheld use
  Inline use
  Various accessories

## Slide 41: Small Volume Nebulizer - Competition
Teleflex Micro Mist
Micro-Mist SVN (Teleflex)
  Basic SVN
  ASP: $0.78 chamber only
  ASP: $1.22 with Mask
  Strong on Contract
  Multiple kit configurations
    High-Efficiency Option (Aero-Tee)
    ASP: $2.36
  Handheld use
  Inline use
  Various accessories
Aero-Tee

## Slide 42: Small Volume Nebulizer - Competition
Salter
Nebutech (Salter)
  Basic SVN
  ASP: $0.61 chamber only
  ASP: $1.10 with mask
  Some contract positions
8900-Series (Salter)
  Basic SVN
  ASP: $0.94 (expensive)
  Minimal GPO contract positions
  Salter focuses on homecare market
NebuTech
8900-series

## Slide 43: Small Volume Nebulizer - Competition
West Med – Vix One
Vix-One (Westmed)
  Basic SVN
  ASP: $1.00
  Minimal contract positions
Vix-One

## Slide 44: High Efficiency Nebulizers
AeroEclipse
Breath Actuated Nebulizer (BAN)
AeroNeb Nebulizer

## Slide 45: Aeroneb®
Advanced medication delivery
  Built intoventilator
  Reusable & autoclavable
  Efficient delivery
    2.4 micron size (MMAD)
    >80% drug less than 5 microns
  Connects directly into the ventilator
  Controlled via the ventilator
    Gas Module is turned off during nebulizer treatment
Tidy up

## Slide 46
Product line extension of the Aeroneb® Pro nebulizer
Provides the user with the choice of a disposable or reusable product – therefore does not replace the Aeroneb® Pro

## Slide 47: Small Volume Nebulizer - Competition
AeroEclipse (Monaghan)
Breath-Actuated Technology
    Nebulizes only during inspiration
    Patient receives more medication
    Reduces caregiver exposure
    Lengthens treatment time (same dose)
    Expensive = $5.00 ASP (US) vs. $0.80 – $1.20 SVN
    Has two modes: “BAN” & “Continuous”
        Use with mask = continuous mode only

## Slide 48
Volume Incentive Spirometers (VIS)

## Slide 49: Lung Management Products
Vyaire Incentive Spirometers
An incentive spirometer is used to examine the health of your lungs by measuring inspiratory volume. This means that an incentive spirometer measures how well you are filling your lungs with each breath.
001902A
001900
Volumetric Incentive Spirometer
Airx Flow
Incentive Spirometer

## Slide 50: Lung Management Products
Vyaire Incentive Spirometers
Incentive Spirometer Options
  Flow (4%) & Volume (96%)
  One-way valve and w/o one-way valve (82%)
  Pediatric w/ colorful targets
P/N | Description | Pckg
001900 | AirLife Air-X Flow IS | 20/case
001902A | AirLife Volume IS, 4000 mL | 12/case
001904A | AirLife Volume IS, 2500 mL | 12/case

## Slide 51: Lung Management Products
Incentive Spirometer – Competition
Voldyne (Teleflex)
  Options: 5000 mL, 2500 mL and Ped 2500 mL
  Does not include one-way valve

## Slide 52: Lung Management Products
Incentive Spirometer – Competition
Coach 2/CliniFLO (Smith’s Medical)
  Offer both with and w/o one-way valve
  O2 connection for supplemental oxygen deliv
  CliniFlo for low flow applications
Smith’s CliniFLO IS
Smith’s Coach 2

## Slide 53: Questions
Thank you!