## Slide 1: Laryngoscopes – sunmed portfolio

## Slide 2: Intro to Laryngoscopy
Laryngoscopy (la·ryn·go·sco·pi ): Laryngoscopy is a term describing the visualization or examination of the larynx by distraction of the upper airway structures.
It is typically used to enable intubation and airway management in anesthesia, critical care, and trauma scenarios.

## Slide 3: Airway anatomy
Notes: The pharynx is a tube formed by skeletal muscle and lined by mucous membrane that is continuous with that of the nasal cavities
The pharynx is divided into three major regions: the nasopharynx, the oropharynx, and the laryngopharynx
The nasopharynx is flanked by the conchae of the nasal cavity, and it serves only as an airway. The uvula is a small bulbous, teardrop-shaped structure located at the apex of the soft palate. Both the uvula and soft palate move like a pendulum during swallowing, swinging upward to close off the nasopharynx to prevent ingested materials from entering the nasal cavity. In addition, auditory (Eustachian) tubes that connect to each middle ear cavity open into the nasopharynx. This connection is why colds often lead to ear infections.
The oropharynx is a passageway for both air and food.

## Slide 4: Airway view in supine position

## Slide 5: Key Airway Anatomy for Laryngoscopy:
Glottic opening (tracheal opening)
Glottic opening: the opening between the vocal cords. This is the target for tracheal intubation.
Vallecula (val·lec·u·la): the space between the base of the tongue and the epiglottis
Arytenoid cartilages (ar·y·te·noid): A pair of small triangular cartilages in the larynx that help to move the vocal cords

## Slide 6: Introduction to Laryngoscopes
A laryngoscope (la·ryn·go·scope) is used to lift the upper airway structures, such as the epiglottis, out of the way to allow visualization of the vocal cords (larynx) and enable intubation through the glottic opening.
Laryngoscopes are used where-ever tracheal intubations are performed, including OR, ED, ICU, NICU, PICU, EMS

## Slide 7: Optional videos
Good views from practioner’s POV
https://www.youtube.com/watch?v=4V_pouIbcnA
Direct Laryngoscopy https://www.youtube.com/watch?v=AZeBumPaj4g
Use of Mac and Miller blades for intubation
Anatomy and Intubation
https://youtu.be/iOPpSGbuYmQ
Skip to the 6:30 min mark: @ 6:30 Anatomy; Great view of vallecula lift at 7:30 / Mallampati overview
@ 8:30 Intubation Equipment; @ 12:00 Direct laryngoscopic intubation
The first 6.5 mins are pharmacology – double back to it if you can
Intubation using Direct and Indirect (Video) Laryngoscopes
https://www.youtube.com/watch?v=gnkYGRMaw7o
First 6 min shows use of different direct and video laryngoscopy devices

## Slide 8: Objectives & Content Outline
Session | Deliverables
Laryngoscopy Intro | Review of Key Basics Market Overview
Product Details | IntuBrite Products Competitive Products
Sales Process | Clear sales process Targeting Detailed Talk Track Evaluation planning & management FAQs/ Objection Handling
Planning Your Success | Intubation training Leading an Effective In-Service
You will have the knowledge, tools, support and target list to be successful with IntuBrite Day 1 post-NSM

## Slide 9: Why is IntuBrite so Exciting?
Patient Safety Reduced HAI Risk with Disposables
Salter Opportunity
Significant account value, GPO Contracts
Clinician Preference Enhanced Visibility and Ease of Intubation
Notes: Hospital acquired infections are an area of increasing concern to hospitals, driving a trend towards use of disposable handles and blades. IntuBrite is well positioned to capture the benefits of this trend.
IntuBrite products are proven. The clearly differentiated lighting system and high quality products are recognized and valued by clinicians
The growth opportunity for Salter is SIGNIFICANT, with OR disposable accounts commonly >$100K annualized value and major GPO contract positions with >$10M potential value.

## Slide 10: IntuBrite Demo Kits
Demo Kit Contents:
Dual LED Disposable Handles & Blades
Greenlight Disposable Handles & Blades
VLS Edge Video Laryngoscope, Reusable Blades, Wands, Rigid Styles, Disposable Sheaths, Accessories
Competitive Disposable Samples: Flexicare, Teleflex Rusch
Misc accessories: Cases, PFHV & STLT, cloth

## Slide 11: POP QUIZ
Glottic opening (tracheal opening)
F
B
C
A
D
E
Glottic opening: the opening between the vocal cords. This is the target for tracheal intubation.
Vallecula (val·lec·u·la): the space between the base of the tongue and the epiglottis
Arytenoid cartilages (ar·y·te·noid): A pair of small triangular cartilages in the larynx that help to move the vocal cords
Name the Airway Anatomy

## Slide 12: POP QUIZ:
Which Blade is Mac Style & which is Miller Style?
A.
B.
Miller Blade
- Most common straight blade design
- MiLLer
Mac Blade
- The most common Curved blade design
- MaC

## Slide 13: Blade Sizes – Mac, Miller size ranges
Mac and Miller blades overlap in many, but not all size offerings
Straight blades are preferred for NICU use – reflected in size range of Miller blades.
  000, 00 and 1.5 are important differentiators to NICU and children’s facilities
Size | Patient Size | % of market | Mac | MIller
000 | Small premature infant | Minimal |  | 
00 | Premature infant | 1.2% |  | 
0 | Neonate | 2.8% |  | 
1 | Small Child | 3.7% |  | 
1.5 | Child | 1.2% |  | 
2 | Child | 19.2% |  | 
3 | Adult | 37.5% |  | 
3.5 | Adult | 1.8% |  | 
4 | Large adult | 22.6% |  | 
5 | Extra-large adult | Minimal |  | 

## Slide 14: More Blade shapes
Curved
Macintosh
Mac Reduced Flange
Mac Improved View
Mac Left Handed
Bizzari-Guiffrida
Mac Prism
Polio
Mac Oxiport
Tull Macintosh (suction)
Fink
Upsher Low Profile
Upsher ULX
Flexible
Eversole
Racz-Allen
Oxford Infant
Bainton
Dopuble-Angle
Blechman
Belscope
Henderson
Vital View
Cardiff
Bennett
Flagg
Snow
Heine
Soper
Straight
Guedel
52.7%
0.8%
0.5%
<0.1%
Straight
Miller
Wis-Hipple
Phillips
Tull Miller
Oxiport Miller
Wis-Foregger
Shcapira
Alberts
Michaels
Robertshaw
Wisconsin
Cranwall
Seward
40.0%
1.1%
0.3%
<0.1%
<0.1%
<0.1%
Key Takeaways
> 90% of intubations are done with Mac and Miller blades
Many specialty blades are for Ped/NICU
IntuBrite blades cover > 93% of all intubations
IntuBrite Configuration
Percentages indicate 2017 sales (by % of intubations)

## Slide 15: Blade Design impacts technique
Straight blade (e.g. Miller): Tip goes under the epiglottis and lifts it directly
Curved blade (e.g. Mac) : Tip fits into the vallecula and indirectly lifts the epiglottis

## Slide 16: Fiber Optic (or Greenline) Lighting Systems
>90% of market
Handles and blades built to the Green ISO Standard 7376 can use the term Green, Green System
Indicated by green color coding on blade and handle
Why is this important?
  Indicates compatibility with any other handle or blade that is also “Green”
  Can mix & match disposable & reusable
Fiberoptic LED
AKA: Green Line, Green system
Greenline = ISO 7376
Bulb is in handle
Battery is in handle
Clear “fiberoptic” tube runs light from bulb to tip

## Slide 17: Standard LED Lighting Systems
<10% of market
Generally have a superior lighting system than fiberoptics
  fiber optic pipe degrades light quality
Not compatible with Green systems
Standard LED
AKA: Conventional
Bulb is in blade
Battery is in handle
Electric conduit runs current from handle to bulb

## Slide 18: POP QUIZ
Which illustrates use of Direct Laryngoscopy _____?
A.
B.
Indirect, or Video Laryngoscopy
Direct Laryngoscopy

## Slide 19: Laryngoscopy Market
SALTER LABS CONFIDENTIAL

## Slide 20: Major Competitor Product Offerings
 | Direct |  |  |  | Video | 
 | Standard LED or Proprietary |  | Greenline (FiberOptic LED) |  | Handheld | Rollstand
 | Reusable | Disposable | Reusable | Disposable |  | 
IntuBrite | Handle |  |  |  |  | 
Flexicare |  |  (new) |  |  |  | 
Teleflex Rusch |  |  |  |  |  | 
SunMed |  | Blade |  |  |  | 
Vital Signs |  |  |  |  |  | 
Verathon | Handle | Blade |  |  |  (new) | 
Medtronic |  |  |  |  |  | 
Ambu |  |  |  |  |  | 
Karl Storz |  |  |  |  |  | 

## Slide 21: Salter is positioned to take advantage of laryngoscope market trends
Legacy
Reusable Handle w/ Reusable or
Disposable Blade
Direct Laryngoscopy
Fully Disposable Handle & Blade
Video Laryngoscopy
Patient intubation difficulty
Harder
Easier
Safer
Current Practice
Infection Control Rigor

## Slide 22: Our Greatest Opportunity is Hospitals with Disposable Handles and Blades
Why Hospitals?
Perform 19 out of 20 intubations annually
Leverages our existing relationships
Leverages our acute product portfolio
Why Disposable?
3x the unit growth rate of reusables
  Driven by JCAHO guidelines
  Increased focus on HAI
Ongoing, consistent purchase, not a one time or infrequent purchase

## Slide 23: Reusable  Disposable: JCAHO drives change
Type | Contact | Req
Critical | Enters sterile tissue or blood flow | Sterilization
Semi-Critical | Contacts mucus membrane | High-level disinfection
Non-critical | No- or intact-skin contact | Low-level disinfection
Current Practice:
Correct Practice:
Wipe down between cases
Typically, submerged in solution by central reprocessing
JCAHO citation
FDA and JCAHO follow the Spaulding Classification…
…which results in citations when hospitals are only doing low-level disinfection on handles

## Slide 24: JCAHO Guidelines
https://www.jointcommission.org/standards_information/jcfaqdetails.aspx?StandardsFaqId=1201&ProgramId=46
Laryngoscope blades are processed via either high-level disinfection or sterilization.
Laryngoscope handles, the organization is following the manufacturer's instructions-for-use for cleaning/disinfection guidance.
Packaged
Stored in a way to prevent contamination

## Slide 25: Sterilization Steps & Cost
High cost per intubation: $17-$26
Laryngoscope failure due to wear & tear, improper re-assembly
Risk of cross-contamination resulting from poor cleaning or bacteria that remains
Loss of product , replacement
Time delays in product availability
Diminished light quality over time
From ‘ Flexicare Cost of Reprocessing Brochure’ http://www.briteprosolo.com/images/downloads/Cost%20of%20Reprocessing.pdf

## Slide 26: Accessed 9/20/2017 https://www.welchallyn.com/content/dam/welchallyn/documents/sap-documents/LIT/80021/80021285LITPDF.pdf
Notes: Even if high level disinfection or sterilization is not required, there are a lot of steps in following Handle manufacturer reprocessing instructions. Welch Allyn recommends “Cleaning and intermediate level disinfection’ for their FO handles.

## Slide 27: Accessed 9/20/2017 https://www.welchallyn.com/content/dam/welchallyn/documents/sap-documents/LIT/80021/80021285LITPDF.pdf
Clean and Intermediate Level Disinfection:
Prepare for Cleaning
Separate blade from handle
Prevent handle from drying
Initial Cleaning
Remove the battery
Clean with germicidal wipe
Brush to remove any visible soil
Re-wipe with germicidal wipe and let sit per germicidal wipe instructions
Air dry
Inspect parts and reassemble
Test by attaching to a clean and disinfected blade
Re-wipe all surfaces with germicidal wipe and let sit per germicidal wipe instructions
Store per facility practice

## Slide 28: Simplest way to keep JCAHO complaint
“We use disposable handles and blades”

## Slide 29: Direct Laryngoscopy  Video Laryngoscopy
Drivers of conversion to Video
Clinical advantage of video
  More compelling for less skilled intubationists
  Strong for EMS, ED, ICU
  Less for anesthesiologists
Clinical advantage for difficult cases
Seen as best, newest technology
More affordable technology options

## Slide 30: Video Laryngoscopy Competition for ‘Routine’
Routine
Difficult
EMS
ED
ICU
Planned Intubations
Emergent Intubations
Rugged, high-quality, expensive device with hyper-angled blade for difficult OR intubations.
Portable, simple, inexpensive device with standard blades for field and unexpected intubations.
Video manufacturers trying to capture the big prize: routine use for all OR intubations.
Two video Approaches

## Slide 31: Major players by segment
* Reusable includes disposable blades used with reusable handles
Fully Disposable | 
Flexicare | 65%
Teleflex | 21%
IntuBrite | 12%
All Others (Heine, Welch Allyn, OPB, Sun-Med, Tri-Anim, Vyaire) | 2%
Reusable | 
Vyaire | 19%
Teleflex | 16%
Sun-Med | 10%
Tri-Anim | 8%
Welch-Allyn | 7%
Heine | 6%
Propper | 5%
Flexicare | 5%
All Others Armstrong, Mercury, Medline, Sharn, Anesthesia Service, > 30 others | 24%
Video | 
Verathon | #1
Karl-Storz | #2
Medtronic | #3
Ambu | #4
Others Teleflex, Venner, McGaw, DRE, Pentax | Minimal

## Slide 32: OTHER TOOLS & INFORMATION

## Slide 33: Reusability
Key Takeaways
All the money is in disposables.
Winning disposable blades only to use with current reusable handles is a pot. wedge
Winning reusables is unlikely. Don’t devote time here.
Reusable
Reusable items are designed to withstand reprocessing (high-level disinfection or sterilization). Most are guaranteed for duration (e.g. 5-7 years) and/or a defined number of autoclave cycles (e.g.) 4,000. Often, the electronic parts (bulb, battery, etc.) can be replaced when broken
Disposable items are designed for single-patient use.
Disposable
Chart: Intubations and Sales by Product Type
| Fully Disposable | Reusable Handle, Disposable Blade | Fully Reusable
Intubations | 1.9 | 1.1 | 16
$ Sales | 22.5 | 5.8 | 5.8

## Slide 34: Reusable vs Disposable: Trade offs
Reusable Handle & Blade
High quality weight and feel
What most physicians are accustomed to using – viewed as the gold standard
Disposable Handle & Blade
Not perceived to have the quality of a reusable
Cost is more ‘tangible’ to department
Environmental impact perceived to be more than reusable
Benefits
Drawbacks
Performance failure/variability due to reprocessing wear & tear
  Light quality degrades/ flicker
  Battery failure, incorrect reinstallation
  Component failure
High initial capital investment
Maintenance & replacement
Reprocessing time & costs (chemicals, time, labor, supplies)
Fresh battery and light for each use
No maintenance or reprocessing resources
Single patient use – no risk of cross-contamination

## Slide 35: Reusable  Disposable: Compliance challenges
$
$
Cost of high-level disinfection
Cleaning solution and sterile water
Labor costs
Switching to high-level disinfection of handles is expensive
Must invest in many more reusable scopes
Go from 1 set per OR to multiple sets per OR to cover time while being cleaned
Higher breakage and loss rates during cleaning
Compliance to high-level disinfection is impractical
Staff are frequently non-compliant
Unanticipated breakage due to
  Leaving batteries in handle during cleaning or incorrect insertion
  Losing scopes during transport
  Faster wear-and-tear due to reprocessing
$17-$26 per intubation for reprocessing handle and blade
Going disposable is the simplest way to stay compliant
Customers are reluctant to believe this

## Slide 36: Cost of Reprocessing Reusable Laryngoscopes
Glendale Adventist Hospital
Glendale, CA
Reprocessing cost $25.97/intubation
If 1 HAI: Add’l $8/intubation
Southeast Health
Cape Girardeau, Missouri
Reprocessing cost $17.12/intubation
If 1 HAI: Add’l $10.28/intubation

## Slide 37: Market segment sizes and growth
Chart: Unit Sales by Year (2013 = 100%)
| 2013 | 2014 | 2015 | 2016
Reusable Handles | 1 | 1.0101 | 0.81818 | 0.74747
Disposable Handles | 1 | 5.86 | 14.74 | 21.72
Video Blades | 1 | 7.1739 | 7.5217 | 7.913

## Slide 38: Market size
Chart: 2016 Market Size ($ millions)
| Reusable | Disposable | Video
Series 1 | 18.4 | 20.8 | 50
Chart: Annual Intubations (millions)
| Hospital | EMS
Sales | 19 | 1
* Reusable includes disposable blades used with reusable handles
Salter’s greatest opportunity is in the Hospital market with Disposable handles & blades

## Slide 39: Major products, pricing, strengths and drawbacks: Disposable
Teleflex
DispoLED
ASP
$10-15
Heine XP
OBP
Surescope
Storz
Laryngobloc
Sunmed SunOne
Smaller Players (not comprehensive)
Flexicare
BritePro
Intubrite
$10-15
$11-12
Strengths
Weaknesses
Recycling program
Contracts
Reliability
Handle-blade give
None
Reliability
Light quality
Handle-blade give
UV light
Light quality
Metal construction
Reliability, strength, and quality

## Slide 40: Major products and pricing: Video
ROLLSTAND
Verathon Glidescope
Karl-Storz C-MAC
Monitor
~$5k
Blades
Cable
Wands
Blades
HANDHELD
Venner APA
dist. by Vyaire
Magaw Co-Pilot
Airtraq
Dist. by TFX
Ambu
King Vision
Medtronic
McGrath MAC
Smaller Players (not comprehensive)
$1.0-$1.5k
$1.6-$2.6k
Sometimes free
Over $5k
$2-3k
~$4k
N/A
N/A
Reusable Config
Disposable Config
~$20-30
$8-10
$12-20
unknown
unknown
N/A
N/A
~$500
~$4k
included
included
~$5-$6k
Intubrite VLS 8800
Intubrite 6600 Edge
$4-$5k
$1k
N/A
$1.5 - $2.5k
$1k
~$1k
~$1k
$8-10
$8-10
Karl Storz C-MAC PM
Verathon Glidescope Go (NEW)

## Slide 41: Questions?